## Slide 1: Using a Compass
Unit: M09U04
By: Alix Flavelle
Notes: <number>

## Slide 2: Uses of a compass
To measure direction (bearings)
To plot locations on a map (triangulation)
To do a compass survey (traverse)

## Slide 3: The compass
Parts of a typical
base plate compass
Notes: There are several different types of compasses. The base plate compass is common. Naming the parts of the compass indicates the essential function of a compass.
<number>

## Slide 4: Magnetic declination
The legend of a topographic map shows:
  magnetic north;
  grid north;
  true north
Adjust the compass when using it with a map.
Notes: The mechanics of adjusting the compass are different depending on the type of compass. The amount of declination (i.e. the angle) is different depending on where on the Earth you are. Declination changes with time so the calculation depends on the number of years from the time the map was made to the current year.

## Slide 5: Taking a bearing to an object
Hold the compass flat.
Hold your arm stretched out.
Sight on the object.
Read the bearing.
Notes: Bearings are measured in degrees. There are 360o on the compass rose or the compass dial. Recall Exercise No. 8 “Compass Rose Race” in M09U01. It is best to learn to use a compass by doing the Exercise No. 1 “Using a Compass” in this Unit.
<number>

## Slide 6: Plotting bearings on a map
Set the bearing on the compass dial.
Lay the long edge of the compass on the known point (where the bearing was taken from).
Turn the compass plate so that the north lines align with the north lines on the map.
Notes: Practise this in Exercise No. 2 “Finding Bearings on a Map”.
<number>

## Slide 7: Taking bearings off a map
Align the base plate with an imaginary line between two points on the map.
Turn the compass dial until the north lines align with the north lines on the map.
Read the bearing set on the compass dial.
Notes: Practise this in Exercise No. 2 “Finding Bearings on a Map”. Note that an alternative way to find bearings on the map is by using a protractor. Note that a protractor will always measure the grid north. Be aware then of magnetic declination and whether your compass is measuring magnetic north or has been adjusted to grid north.
<number>

## Slide 8: Triangulation
Resection - bearings to two known locations to determine an unknown location
Intersection – bearings from two known locations to determine an unknown location
Triangulation – third bearing to verify
Notes: Once you are familiar with finding bearings on a map, you can see how triangulation works. Triangulation has become a generic term for the process of measuring to two or more known points to determine - using geometry - the location of an unknown point. In fact, there are three methods as shown in this slide. Practise triangulation in Exercise No. 2, “Finding Bearings on a Map”.
<number>