## Slide 1: Compass Survey
Part 1: Conducting a compass survey
Unit: M09U04
By: Alix Flavelle
Notes: <number>

## Slide 2: Uses of a compass survey (or traverse)
Map very small areas
Map in a lot of detail
Learn basic principles of scale mapping

## Slide 3: Measure direction and distance
Direction is measured by:
  compass.
Ground distance is measured by:
  metre tape;
  surveyor’s “chain”;
  rangefinder.

## Slide 4: Slope distance to horizontal distance
Slope distance on the ground must be “flattened” to horizontal distance.
Measure slope angle with:
- clinometer;
- slope needle on compass;
- handmade clinometer.
Calculate horizontal distance.

## Slide 5: Calculating horizontal distance
Use the equation:
Horizontal distance = slope distance x cosine of slope
Notes: Practise calculating slope in Exercise No. 4, “Measuring Slope and Making Slope Conversions”.
<number>

## Slide 6: Planning the traverse route
Select a starting point.
Plan the route with a sketch map.
Choose from four traverse patterns:
  linear traverse;
  radial traverse;
  grid traverse;
  closed traverse.
Notes: The starting point should be a recognisable and permanent landmark so that the traverse can be replicated. The starting point should be considered as a “tie point”, a concept introduced in M09U02.
In participatory mapping, a sketch map is always prepared before commencing scale mapping. The sketch map serves as a discussion tool to plan the scale mapping or, in this case, the compass traverse. Planning the route is important so that all of the survey team members know where they are going. There may be more than one team and more than one route (e.g. if using a radial traverse or two closed traverses). Thus, tie points are important.

## Slide 7: Linear traverse
Follows a line such as a road or stream

## Slide 8: Radial traverse
Several linear traverses starting at one point
Useful when trails radiate from a village centre

## Slide 9: Grid traverse
Parallel linear traverses forming a grid
Allows systematic mapping of an area
Often used for resource inventories

## Slide 10: Closed traverse
Follows the perimeter of an area or territory
Allows for the calculation of area

## Slide 11: Conducting a compass traverse
Need minimum of two people
Start at the Point of Commencement (POC)
Measure distance and bearings from each station to the next

## Slide 12: Organising the team
“The leader” goes ahead.
“The scout” scouts ahead of the leader.
“The compass person” takes bearings.
“The recorder” records data.
“The note taker” takes extra notes and draws sketches.

## Slide 13: Recording the traverse
Sketch in features
Side shots
Intersection technique

## Slide 14: What to record
Determined after discussion with the community
Examples:
  historical places
  sacred sites
  local place names
  land use
  forest products
  hunting areas
  natural landmarks
  fishing areas
  land ownership

## Slide 15: Setting up the notebook

## Slide 16: Compass Survey
Part 2: Plotting the compass survey

## Slide 17: Steps to plot the survey
  Determine an appropriate map scale.
  Prepare graph paper.
  Convert slope distances to horizontal distance.
  Convert horizontal ground distance to map distance.
  Plot bearings and distances.
  Calculate error or a closed traverse.

## Slide 18
Determine an appropriate map scale
scale = length of traverse (cm)
length of paper (cm)

## Slide 19
2. Prepare the graph paper
Cut to a desired size.

## Slide 20
3. Convert slope distance to horizontal distance
Horizontal distance = slope distance x cosine of slope
Notes: Make the slope conversions for all of the field data. If there is an extra column in your field notebook, write the conversions there. Otherwise prepare a new sheet for bearings, slope distance, horizontal ground distance and map distance.
<number>

## Slide 21
4. Convert horizontal ground distance to map distance
map distance = ground distance (cm)
scale
Notes: <number>

## Slide 22
5. Plot the bearings and distances on graph paper using a protractor and ruler
Locate the POC
Place protractor and mark the bearing:
  place ruler and measure the distance
  mark the station with a small triangle and write in the station number
  move the protractor to station #1 and continue

## Slide 23: Calculating error
Measure the gap between the starting point and the end of the last line.
Add all the distances in the notes to find the perimeter of the traverse.
Calculate percent error using this equation:
Percent error = gap (cm)
perimeter (cm)
Notes: Calculating error can only be done for a closed traverse.
<number>