## Slide 1: Data collection for scale mapping
Unit: M09U02
By: Alix Flavelle
Notes: <number>

## Slide 2: Data collection for scale mapping
Overview of methods for making scale maps
Selecting the method
Concepts for collecting quality data
Best practice in taking field notes

## Slide 3: Overview of data collection methods for scale mapping
Drawing on existing scale maps
Using a scale map with a compass
Compass traverse
Global Positioning System
CyberTracker
Notes: This overview is intended to give a picture of the full range of data collection methods for scale mapping. Not all methods are used in every mapping project. If it is already known which methods the training will address, those methods should be emphasised.

## Slide 4: Drawing on existing scale maps
Quickest way to make a scale map
Useful for large areas (i.e. 1,000 km2 +)
Adequate accuracy for small-scale maps
Need well-defined topography
Relies on good facilitation
Notes: More on working with base maps in Unit 3.

## Slide 5: Map and compass
Triangulation using compass bearings or using a laser rangefinder allows scale mapping at a distance
Must be able to sight on topographic features (i.e. access to viewpoints)
Plot bearings on geo-referenced base map
Combine with GPS survey by taking bearings from waypoints
Notes: More on using a map and compass is presented in Unit 3. This is one of the more difficult methods of mapping because it requires a good understanding of compass use, map interpretation and geometry. It also requires a certain amount of strategic planning.

## Slide 6: Compass traverse
Measures distance with a metre tape (or other instrument) and direction with a compass
Good for mapping small areas in detail
Hands-on approach demonstrates clearly the principles of scale mapping
Notes: A compass traverse or survey is perhaps the most basic method of mapping because it follows a simple step-by-step process. More about doing a compass traverse is presented in M09U04.

## Slide 7: GPS survey
Quickest way to collect lots of spatial data
Requires getting out on the land and walking the survey
Data can be used to draw maps from scratch
Data can be plotted on a base map with the advantage of visualising the landscape
Notes: GPS is a versatile and useful mapping tool, essential for scale mapping of larger areas. Operating a GPS unit and collecting coordinate points are very easy. Understanding how the system works can be challenging because the concepts are quite abstract. More about this is presented in M09U05.

## Slide 8: CyberTracker
Installed on a hand-held digital device such as a PDA or smartphone
Attached to a GPS
Uses customised screens with icons and text to enter observations
Highly efficient way to gather large quantities of geo-referenced field observations
Notes: CyberTracker is essentially a very efficient way to collect GPS data.

## Slide 9: Selecting a data collection method
Purpose of the mapping effort
Size of the area
Topography
Level of precision required
Type of thematic maps needed
Cost of the equipment and training
Notes: If the training is taking place for a particular mapping project, initiate a discussion about how each of these factors applies to the context of the training.

## Slide 10: Concepts for collecting quality data
Data integrity
Precision, resolution and accuracy
Triangulation
Absolute and relative locations
Survey tie points
Map interviews
Notes: This is an overview of the concepts. Concepts are best understood in practice. Invite participants to notice which concepts arise in each of the various exercises in this Unit and others throughout this Module. Also consider how each of these concepts relates to the particular context or mapping project associated with the training.
<number>

## Slide 11: Data integrity
Essential for the maps to be credible
Cornerstones of data integrity:
  traceability
  consistency
  verifiability

## Slide 12: Resolution, precision and accuracy
Resolution – fineness of the measuring device or scale
Precision – fineness of the measuring device or scale, plus the human factor and the targeted accuracy
Accuracy – the actual correctness of the data, as it fits reality
Notes: These terms are often mistakenly used interchangeably. They are not interchangeable, but the concepts are interrelated. You can use a precision measuring device to measure someone’s height and state that she is 160.75 centimetres. However, because you neglected to notice she is wearing high-heel shoes, your measurement is not accurate. She is actually 158 centimetres tall. Another example from mapping: On a 1:50,000 scale map, the resolution is such that a 1 mm pen mark would represent 50 metres on the ground. Because it is impossible to draw to submetric precision, is it necessary to use survey tools with submetric precision.

## Slide 13: Spatial accuracy
Whether the measured and mapped location is within a certain distance of the actual location
  acceptable level of accuracy depends on the purpose of the map
  appropriate resolution and precision of the tools and methods depends on the accuracy desired

## Slide 14: Attribute and conceptual accuracy
Attribute accuracy = how correctly the attribute data is described and drawn
Conceptual accuracy = how correctly the map depicts community members’ conceptual view

## Slide 15: Attribute and conceptual accuracy
Attribute and conceptual accuracy depend on:
  an acceptable level of participation and representation;
  a systematic methodology for documentation, interviewing and note-taking;
  opportunities for verification, correction and revision at the community level.
Notes: <number>

## Slide 16: Triangulation
A way to cross-check attribute data
  ask questions of a person in different ways
  ask different people the same question
  ask the same or different person the same question while looking at a place from a different point of view

## Slide 17: Absolute and relative location
Absolute location = coordinate point
Relative location = location measured to or from another location
Notes: GPS measures absolute location. Compass measurements always give relative location.
<number>

## Slide 18: Survey tie points
Noting reference points that allow us to cross-check spatial data by using different survey or cartographic methods
Notes: Tie points are particularly important when dealing with relative locations or in “tying” relative locations to absolute locations.
<number>

## Slide 19: Taking systematic field notes
Advantages:
  allows fast and efficient recording
  reduces questions and errors when processing the data and drawing maps
  shows clearly the method of data collection and lends credibility to the map
  facilitates adding to and updating map data later
Notes: Maps are drawn from a set of data. Often in mapping projects, the person drawing the map may or may not be part of the survey team. Thus, the notes must be clearly and systematically presented so that the map can be drawn correctly.

## Slide 20: Taking systematic field notes
  Prepare a format before going to the field.
  Create enough space for thorough notes.
  Record the date, name of the community or area and name of the surveyor.
  Write neatly.
  Use pencil rather than pen.
  Write notes as if they are a permanent record – they are!

## Slide 21: Describing location in words
Use named landmarks
  a common map reference for everyone
  constantly ask place names
Use local landscape terminology
  make a dictionary to translate local to national language and to describe meaning of terms
Record notes in language of the speaker

## Slide 22: Describing location in numbers
Numbers are a short-hand way to identify a location.
Create a numbering system to keep spatial reference points in order.

## Slide 23: Describing location in sketches
Use to record observations to add in drawing the final map
Takes less time than writing the same observations in words
Two types of sketches:
  panorama
  transect

## Slide 24: Check notes together
Check notes regularly as a team - at the end of each survey day if possible
  easier to do when memory is fresh
  gives opportunity to ground-check, correct and fill in gaps
Check for completeness and consistency