## Slide 1: Making scale maps using existing base maps
Unit: M09U03
By: Alix Flavelle
Notes: <number>

## Slide 2: Making scale maps using existing base maps
Introduction
About base maps
Preparing and customising the base map
Drawing local knowledge on the map – the process and the mechanics
Transferring information from a sketch map to scale
Verifying data through ground-truthing

## Slide 3: The “local map grid”
Conventional cartographers use the coordinate system to geo-reference and locate features.
Local people traditionally use rivers and roads to navigate and this is their “local map grid”.
Draw the map using what is common to both – rivers? roads? mountains?
Notes: <number>

## Slide 4: Base maps
A geo-referenced base map has these conventional features:
  scale
  direction
  visible reference features – such as rivers, roads, mountains
  coordinate system
Notes: A base map with scale and no coordinate system can be used to make a scale map. A grid is not needed to draw community information. With a coordinate system, the map is said to be “geo-referenced”. In order to digitise the map and relate the map to other maps, it must be “geo-referenced”. Geo-referencing can be done later, after the community information is drawn. To assess participants’ level of cartographic knowledge, ask them to suggest ways to geo-reference a map, to add the grid. What tool could be used?
<number>

## Slide 5: Types of base maps
Topographic maps
Remotely-sensed images:
  air photos
  radar photos
  satellite images
  ‘Google Earth’ images
Notes: The two primary sources of base maps are topographic maps and remotely-sensed images. Both have advantages and disadvantages explored here. Usually the choice of what to use is a matter of what is available.
<number>

## Slide 6: Topographic maps
Commonly used
Have all the data required
Difficult to obtain in some areas
Contour lines may be difficult for some people to read
In flatter areas, it is difficult to interpret terrain and rivers can change.
Notes: <number>

## Slide 7: Remotely-sensed images
May be more intelligible for local people than a topographic map – landscape appears more like in a photograph
Vegetation and terrain are visible
Preparation process (e.g. geo-referencing) is generally more complex
Notes: For more about selecting and using remote sensing, see M11.
<number>

## Slide 8: Preparing the base map
Calculate the scale needed
Convert the map scale – enlarge as needed
Customise the base map
Reproduce the base map – by photocopying, scanning or digitising
Notes: Preparing the base maps involves several steps that usually require access to a computer or photocopy machine which are not in the village. In a participatory process, this preparation is often done by a small team which is leading the mapping project. The amount of preparation depends on the base map available and the particular process of the mapping project.
<number>

## Slide 9: Calculating the scale
The scale you choose depends on the:
  size of the area;
  size of the paper you want;
  amount of detail you want to draw.
Notes: The scale of the base map often needs to be adapted according to the size of the land area and the design of the map to be drawn.
<number>

## Slide 10: Calculating the scale
Estimate the size of the area you want to map:
  by identifying topographic features on the map that are at the edges of the area;
  by going to the edges of the area with a GPS unit and plotting them on the map.
Measure the map distance across the area with a ruler.
Notes: <number>

## Slide 11: Calculating the scale
Use the equation:
Desired Scale = width of area in centimetres
width of paper in centimetres
Round the scale to the nearest 1,000

## Slide 12: Changing the scale
If enlarging by photocopy machine:
  enlarging by 200% doubles the size of the map and halves the scale.
  Calculate with this equation:
  Percent enlargement = (scale of original) x 100%
  target scale
Notes: Of course, if the base map is from a digital source, the map will be scaled and sized by computer. A paper base map can also be digitised and then it will be sized using the computer.
<number>

## Slide 13: Customising the base map
Refine the “local map grid” by:
  correcting and adding place names;
  correcting the location of settlements, rivers and ephemeral streams - features that are often wrong and can be located by interpreting the map or by GPS;
  adding local landmark features.
Notes: Certain features may be labeled or located incorrectly on a topographic map. These should be corrected first, so that they don’t cause confusion in the mapping process.
<number>

## Slide 14: Reproducing the base map
Depending on the scope of the mapping project, work with one or many copies.
Carry maps into the field to engage small group discussions.
Two ways to reproduce:
  photocopying
  scanning or digitising to computer – then print.
Notes: <number>

## Slide 15: Drawing community data on scale base maps
The quality of the result is in the amount of map detail and accuracy.
The result depends on:
  distinctive topography;
  a well-prepared base map;
  good facilitation.
Notes: It is better to have more distinctive topography (i.e. rivers, mountains and valleys) to make visible landmarks on the map.
A well-prepared base map includes one with appropriate scale, customised local place names, local highlighted landmarks and colour.
Good facilitation requires taking time to orient community members to the base map and asking good questions.
<number>

## Slide 16: Drawing on base maps – the process
Categorise what to draw on each thematic map.
Design the legend.
Help local people read the map.
Use colour pens.
Notes: More detail about designing the legend is presented in M10.
Take plenty of time to help local people become familiar with the map. Sit around the map, relax, talk about important features in the landscape and point them out on the map. Using colour helps to highlight familiar features.
<number>

## Slide 17: Drawing on base maps – the mechanics
Draw directly on photocopies of the base map.
Alternatively, draw on transparent overlays.
Use colour pens.
Trace rivers and roads first.

## Slide 18: Making thematic overlays
The advantage of transparent overlays is that they can be laid over each other to cross-check and compare.
Tips for making overlays:
  make registration marks;
  use colour pens;
  use transparent material;
  start with the “local grid” e.g. rivers and roads.
Notes: Make transparent overlays of different themes. Each thematic map is then based on the same base map and the base information is consistent. By laying one layer on top of the other, the thematic information on one can be examined against another to check for logical consistency.
<number>

## Slide 19: Transferring sketch maps to base maps
Start with locally relevant reference features (e.g. the local map grid).
Then eyeball the locations for data in between asking local experts questions for clarification.
Refer to field notes to help determine locations.
Notes: Essentially this is the same process as drawing a map from scratch on a base map. It is important to highlight the “local grid” first on the base map. The sketch map provides the reference information to be transferred, rather than drawing from memory. The mental map is drawn already in the form of the sketch map.
<number>

## Slide 20: Ground-truthing and verification
Go out on the ground, measure some locations and see what’s actually there.
Use GPS or a compass and a map.
Reasons:
  allows verification by community members
  adds credibility and validity
  provides opportunity to gather more detailed information and to cross-check
Notes: Ground-truthing may be more or less intensive. Obviously, the more ground-truthing that is done, the more accurate the map. However, then it is no longer table-top mapping, but a survey! Ground-truthing may be done by walking and eyeballing locations from a viewpoint or by measuring sample locations with GPS.
<number>