## Slide 1: Mapping with GPS
Unit: M09U05
By: Alix Flavelle
Notes: <number>

## Slide 2: Introduction: Mapping with GPS
What is GPS?
How GPS works
Types of GPS receivers
Accuracy of GPS
Using a GPS receiver
Designing a GPS survey
Plotting GPS data

## Slide 3: What is Global Positioning System (GPS)?
Determines absolute location on Earth as coordinates from satellite signals
System consists of:
  24 satellites orbiting the Earth;
  a hand-held receiver;
  a control station that monitors the satellites.

## Slide 4: How GPS works
GPS uses the principle of triangulation to three or more satellites.
Satellites travel in a known orbit so their locations are known.
A GPS receiver measures the distance to the satellites “in view” by timing the signal.
It then calculates the position.
Notes: The principles of how GPS works are understood through the concepts of triangulation and that distance is measured by how long it takes a signal to get from one point to another.
<number>

## Slide 5: How GPS works

## Slide 6: Types of GPS receivers
Recreational-quality
Mapping-quality
Survey-quality
Notes: These are generalised categories for the quality of GPS receivers. Like all technologies, the price comes down on GPS receivers as demand increases. A recreational-quality receiver today is the equivalent of a mapping-quality receiver several years ago. Depending on the scope and purpose of the participatory mapping project, a good recreational-quality GPS is usually adequate.
<number>

## Slide 7: Smartphones: Assisted-GPS
Advantages
  A-GPS gets a faster fix
  A-GPS can use weaker signals than most conventional GPS
  uses device someone may already have
Disadvantages
  must be in range of mobile phone network
  may incur charges for connection time
  not built for rugged outdoor use
  not designed for mapping
Notes: <number>

## Slide 8: Factors in selecting a GPS receiver
Sensitivity of antennae
Number of channels
Data logging capacity
Range of datum selections
Data output capability
External antennae
Mask angle
Waterproof and durable
Battery life

## Slide 9: Accuracy of GPS: constant factors
Satellite clock error
Ephemeris error
Receiver clock error
Atmospheric disturbance to the signal
Notes: These are sources of error that we cannot do anything about except be aware of them. Developments in GPS technology are mostly about how to improve accuracy by compensating for these sources of error.
<number>

## Slide 10: “Controllable” sources of error
When satellites are clustered in one region of the sky, the position calculation is less accurate.
good poor
What to do? You can move or wait.
Notes: It is important to understand these controllable sources of error so that you may avoid or troubleshoot problems.
<number>

## Slide 11: “Controllable” sources of error
Reflected signals: Signals can be reflected off terrain features and the GPS receiver confuses the reflected signal and the direct signal.
What to do? Be aware and cross-check coordinates when in steep and complex terrain.

## Slide 12: Adjusting a GPS to local area
Coordinate system
Distance and elevation units
Time
Datum
Notes: These are the units that need to be adjusted in order to operate the GPS effectively in the local area. The instruction book with the GPS unit will explain how to adjust these settings. We will do this in Exercise No.1, “Using a GPS Unit”.
<number>

## Slide 13: Using a GPS receiver
Let the receiver “wake up”.
Read the coordinate.
Check the sky map and signal strength.
Mark waypoints.
Alternatively, begin a track.
Record the waypoint and notes in the field notebook.
Notes: Operating a GPS unit is very simple.
<number>

## Slide 14: Designing a GPS survey
Identify priority areas, tracks, points and what information to record there.
Determine criteria for waypoints.
Determine criteria for tracks.
Create a numbering system.
Notes: These are things to consider in designing a GPS survey. Discuss what information to collect and where. It is a matter of strategising the best use of time, the priority sites and areas to map. What things should be mapped as lines; the data for those might be collected as tracks. What sites will be mapped as point data and therefore collected as waypoints? What sites will have a lot of notes or whole stories written for them and therefore need to be recorded as waypoints and identified? Is there just one GPS unit and one team? If so, a simple numbering system may suffice. If there is more than one unit and survey team, the numbering system needs to be coordinated.
<number>

## Slide 15: Plotting GPS data
Find the numbers on the sides or top and bottom of the base map.
Interpolate the numbers in between to find the exact coordinate.
Use a straight edge or grid tool to locate the point in the centre of the map.
Notes: The interpolation is a mathematical process and takes some practice to understand well. A grid tool (a template made to fit the grid) reduces the calculation required. Practise plotting in Exercise No. 3.
<number>

## Slide 16: Plotting GPS data: latitude-longitude
Example: if the numbers at the side are 115o and 120o, then divide and subdivide like this:

## Slide 17: Plotting GPS data: UTM
Division is always by ten’s
Units relate to metres on the ground
Notes: The hand-drawn numbers are those that are not marked on the actual map. They are the numbers measured (interpolated) between.
<number>

## Slide 18: CyberTracker system
Software designed to efficiently record large quantities of geo-referenced field observations
Installed on a computer, customised and then uploaded to a PDA or smartphone that is used with a GPS
After collecting data in the field, it can be viewed on the computer as reports and maps
Notes: Cybertracker is a very efficient way to record GPS data and generate maps.
<number>

## Slide 19: A CyberTracker database
Field observations are recorded using customised screens and icons.

## Slide 20: CyberTracker maps
Connect a GPS to the PDA by cable.
View field map on a PDA; use it to navigate or to pinpoint locations using a stylus where a GPS fix cannot be obtained.
Download data to a computer and use mapping functions to make maps in Cybertracker.
Export database to MS Excel, ArcView or other mapping software.
Notes: See the video with this Unit and Additional Resources for more detail on what Cybertracker can do and how to use it.
<number>