## Slide 1: Drawing and Producing Scale Maps
Unit: M09U06
By: Alix Flavelle
Notes: <number>

## Slide 2: Introduction
Hand drafting or computer drafting maps
The process of drawing final maps
  organising the survey and map data
  designing the thematic maps
  selecting and tracing from base maps
  making maps from scratch
  verification
Elements on a map
Documentation of source data
Notes: This is the outline of the presentation.
<number>

## Slide 3: Choosing hand drafting or computer drafting
Source data
  compass and paper topographic maps are easily hand drafted
  GPS data and satellite imagery are easily put on computer
Desired process in the community
  is hand drafting more accessible and understandable?
Desired outcome
  the look of the map

## Slide 4: Strengths of hand-drafted maps
More people can see and know how to handle the data
Gives a sense of ownership
Potentially more people can participate
Less training, less capital cost
Presents a customised, hand-drawn feeling to the map

## Slide 5: Weaknesses of hand-drafted maps
Time-consuming to draft, redraft and update
Large amounts of GPS data are slow to process
Reproduction in colour is not always possible
Final map is only in paper format which is not durable; it can warp and fade

## Slide 6: Strengths of computer-drafted maps
Fast to produce (once the system is set up and the data are entered)
Large amounts of GPS data are easy to process
Easily updated, corrected and redrafted
Easily produced and reproduced in colour and at different scales
More options in map design

## Slide 7: Weaknesses of computer-drafted maps
People may lose grasp of where the data went (mitigated by a good verification process)
Not as accessible for rural villagers
Tendency for maps to have a “cookie-cutter” look (a matter of skill in design)
High cost in training and equipment
Tendency for computer technology to mask poor quality data

## Slide 8: The process
Organise the survey and map data.
Design thematic maps.
Select and trace from base maps.
Alternatively, draft maps from scratch.
Draft the final map.
Verify the maps with the community.

## Slide 9: Organising the map data
Organise and compile the survey data.
Plot survey data manually or on computer.
Compile rough draft maps and field maps.
Compile thematic maps from other sources and adjust the scale.

## Slide 10: Designing thematic maps
An aspect of map design
Categorise - what information will be shown on each different “map layer”?
Design the legend with:
  items common to all layers;
  items specific to each layer.
Notes: In a participatory mapping project, there already will have been discussions about what type of information to map. Discuss with participants what kinds of thematic maps they could envision making in their community and brainstorm to make a list of specific legend items for each theme.
<number>

## Slide 11: Building the map layers
Trace or digitise selected information from the rough maps.
Add data from field notes.
Select first the information common to all the layers
  e.g. rivers, boundaries, roads, settlements.
Continue selecting and tracing community data to each thematic map in the series.

## Slide 12: Scale maps made from scratch
Made from compass traverse or GPS data
The survey track is the “base map”
Disadvantages:
  rivers and roads, the “local grid”, must be surveyed too
  time-consuming to collect thematic information
Notes: Maps are made from scratch when there is no base map available. It is time-consuming to survey the “local grid” and enough thematic information. So maps from scratch are often made for a specific purpose. Compass surveys are normally drawn from scratch, by hand or by computer. They are usually made for a small area and specific purpose. GPS survey data are more often mapped on, or combined with, base map information.

## Slide 13: Checklist of essential map elements
Map title
North arrow
Scale
Grid
Legend
Location map
Notes: These are standard elements on all scale maps.

## Slide 14: Optional notations
Copyright statement
Explanatory note
Map series number
Signatures of validation
Notes: Whether to include these optional notations depends on the purpose of the map and the design of the map series.
<number>

## Slide 15: Document source data on map
Base map reference
Thematic map reference
Survey information – when, who
Source of thematic information – who provided the community information
Notes: On the map, the source data are identified in brief.

## Slide 16: Meta-data documentation
Catalogue and store original source data.
Create a meta-data document for:
  coordinate system and datum;
  magnetic declination;
  pen sizes and templates for hand drafting;
  fonts, colour codes, symbol codes;
  list of computer file names;
  names of those involved in surveying, drawing and supplying map information.
Notes: In separate documents the meta-data are recorded and stored. The meta-data tell us how the map was made and how to find the data that were used – if ever we wanted to recreate the map.

## Slide 17: Verification process
Community members must have an opportunity to verify that the information they contributed was drawn correctly:
  in a single or series of community meetings;
  with the community as a whole or with the knowledge sector;
  effectively done in small groups;
  taking time to explain the maps in simple language.
Notes: The verification process will vary according to the design of the mapping project, its scope and the number of people or communities involved. It is important to start immediately while interest is high and the mapping is fresh in everyone’s mind. Allow ample time in a session to make sure that people understand the maps. Allow ample time to give feedback even if it means scheduling a few sessions over a few weeks. At the same time, be careful not to lose momentum and interest by allowing it to drag on too long.

## Slide 18: Correcting and updating maps
Survey and ground-check corrections as needed.
Re-draft maps as needed.
Verify again.
Notes: Verification and correction is an iterative process. The more thorough and participatory each step, the fewer iterations needed to get it to the point where the maps are validated.