## Slide 1: Georeferencing for Digitising
By: Willy Kock and Jeroen Verplanke, ITC
Unit: M10U04
Notes: Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>
Note for the presenter: Before delivering this presentation please read the Handout for Trainee of Unit M10U04.

## Slide 2: Digitising
Capturing data by converting features on a paper map or (digital) aerial photograph into digital vector format
Notes: This is the definition of the term “digitising” as a concept in GIS. Of course, there are other dictionary meanings for the word in other contexts.
Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 3: Digitising methods
Method | Devices
Manual digitising | Coordinate entry via keyboard Digitising tablet with cursor Mouse cursor on the computer monitor: on screen digitising (heads-up) Digital photogrammetry
Automatic digitising | Scanner
Semi-automatic digitising | Scanner and line-following software
Notes: Manual digitising with a mouse cursor on the computer screen is currently the most practised method. It requires coordinate entry via a keyboard.
One can use a digitising tablet as an alternative to using a mouse, but this equipment is less commonly available.
The software used to do the digitising must have digital photogrammetric functionality (from GIS). In principle, digitising can be done in any image and photo editing software, but it is essential to use GIS software to derive a geometrically correct map with coordinates.
Automatic and semi-automatic digitising require pre-programmed advanced techniques that are useful only if digitising is a repetitive and frequent task. They are unimportant methods in this case.
Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 4: Digitising methods
Notes: Different approaches are possible to add the information from a 3D model into a spatial database.
In this figure we follow the red line:
The starting point is the digital photos taken of the model (DOCUMENT).
We do not require scanning but we can directly go to on-screen digitising where we open the RASTER image (photos) and vectorise the different features of the 3D model
The VECTOR map that is finally derived can be added to a geodatabase containing other GIS data (e.g. digital versions of the base map of the model).
Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 5: Manual digitising
Two methods for manual digitising:
  Tablet digitising
  On-screen digitising
Notes: In this Module, we only cover the preparations for on-screen digitising.
Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 6: On-screen vs. tablet digitising
More comfortable for the operator
More accurate: zooming facilities
Faster: semi-automatic, digitising and editing at the same time
Updating procedures: geometrically corrected satellite imagery and scanned aerial photos can be overlaid with the old vector data
Notes: Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 7: On-screen digitising: What do you need?
Scanning and image-editing software
GIS software (QGIS, ILWIS, ArcGIS)
Notes: Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 8: On-screen digitising procedure
Open/import an existing raster layer (photo) into your GIS program
The image will be shown on the screen
The features can be traced by a mouse
The x, y coordinates of these features are recorded and stored as spatial data
First georeference the photos
Notes: Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 9: Georeferencing: What to do?
The image is a photo of the 3D model
Data are not yet structured into classified and coded objects
Image data has to be vectorised and structured first
Notes: Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 10: Georeferencing: What to do?
Establish control points from the base map
At least four points with known coordinates should be marked on the map
Notes: Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 11: Georeferencing: What to do?
Write down the x, y coordinate of each point
Notes: Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 12: Georeferencing: What to do?
Georeferencing the image: typing coordinates
  Use the software's georeferencing tools to select and add control points
Notes: Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 13: Georeferencing: What to do?
Click the mouse pointer over a known point on the raster layer for which you have the x and y coordinates
click
Notes: Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 14: Georeferencing: What to do?
After you add at least four points, you can evaluate the transformation.
In most GIS software, you can examine the “residual” error for each point and the “RMS” (Root Mean Square) error.
In the ideal situation, the RMS error should not be greater than one pixel.
Notes: Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 15: Georeferencing: What to do?
Table shows residual errors of control points resulting in an RMS error greater than one pixel
Notes: Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 16: Georeferencing: What to do?
If RMS is greater than one pixel, delete the control points with the greatest residual errors and create new points.
Notes: Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 17: Georeferencing: What to do?
RMS smaller than one pixel: OK
Notes: Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 18: Georeferencing: What to do?
The actual procedure for georeferencing is different for each software program.
Check the software to help guide you about this process.
Notes: Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 19: On-screen digitising: What to do?
Before you start to digitise the images, it is best to stitch different overlapping images of the model together.
The actual procedure for “stitching” is different for each software program. Check the software to help guide you about this process.
Notes: Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 20: On-screen digitising: What to do?
When your image is completely georeferenced and stitched, you can start on-screen digitising by tracing the features in a new vector layer.
This method is covered in M12U04.
Notes: Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>