## Slide 1: The P3DM Process
Various phases
By: Giacomo Rambaldi
Unit: M10U01
Notes: <number>
Note for the presenter: Pleaser refer to the Handout for Trainee (Handout4T) for more information and for preparing to deliver this presentation.

## Slide 2: Flow of the presentation
Preparatory phase
Manufacturing the blank model
Data input
Data extraction
Notes: <number>

## Slide 3: The Preparatory Phase

## Slide 4
Preparing the
logistics
Procuring inputs
Preparing the
base map
Sourcing for spatial
data (contours)
Preparing the agenda
Preparing the
draft legend
Mobilising
stakeholders
Choosing the scale
Defining
the area
Consulting
stakeholders
Obtaining FPWIC
Notes: <number>
FPWIC: Free Prior Written Informed Consent

## Slide 5: Geographical scope
The concerned communities should select the area to be mapped.
Pay attention to the:
  purpose of the mapping exercise;
  watersheds;
  cultural domains;
  zones.
Notes: <number>

## Slide 6: Choosing the scale
1:10,000 scale: 1 cm on the map equals 100 metres on the ground
1:5,000 scale map: 1 cm on the ground equals 50 metres on the ground
At scales smaller than 1:15,000, informants have difficulty precisely locating features
P3DM is best done at scales > 1:10,000
Notes: <number>

## Slide 7: Choosing the scale
Given a defined project area, the choice of scale will determine the size of the model
Notes: <number>

## Slide 8: Preparing the base map
Ensure that:
  contour lines are coloured in a repeating sequence
  labels (many) show elevation in metres
  a grid is added
  the lowest elevation contour line is clearly identified
  you get at least two copies of the base map
Notes: <number>
Grid (10 cm = 1 km on the ground at a 1:10,000 scale)

## Slide 9: Procuring inputs
Procuring inputs is a critical step in organising a P3DM exercise because you:
  cannot run out of materials during the P3DM workshop
  must ensure that all participants are given the chance to actively participate and that nobody feels excluded
  must have enough materials to accommodate the unexpected
Notes: <number>

## Slide 10: Materials to reproduce contour intervals
Carton board
Expanded EVA/PE closed-cell foam
Images by PAFID
Notes: <number>
A physical Participatory 3D model is best assembled using either single wall corrugated carton boards or Expanded EVA / PE closed-cell foam or sponge sheets.
The thickness of the material will determine the vertical exaggeration of the model.
As an example, a 20 metre contour represented by a 4 mm thick material would result in a two-times vertical exaggeration. Vertical exaggeration simply means that your vertical scale is larger than your horizontal scale. The exaggeration is used to emphasise vertical features, which might be too small to identify relative to the horizontal scale.
Expanded EVA / PE closed-cell foam is a lightweight material that has a smooth surface and does not absorb water. Models made out of this material are well-suited for humid tropical environments where carton board may deteriorate rapidly.

## Slide 11: Push and map pins for points
Examples of point features:
  Water point
  Household
  School
  Health centre
Images by Giacomo Rambaldi
Notes: <number>

## Slide 12: Yarns for linear data
Examples of line features:
  Road
  Foot trail
  Water course
Examples of areas:
  Malaria-infested area
  Flood-prone area
Image by Giacomo Rambaldi
Notes: <number>

## Slide 13: Paint for polygons
Examples of point features:
  Grassland
  Water body (lake)
  Paddy field
  Orchard
  Dark forest
  Bamboo forest
  Landslide
Image by Giacomo Rambaldi
Notes: <number>

## Slide 14: Overlapping features
Yarns can be used to add data sets on top of other layers
  For example, a coastal area (light blue paint) is considered a no-touch zone (orange yarn identifies the boundaries of the zone)
Notes: <number>

## Slide 15: Scaling and referencing
Image by Giacomo Rambaldi
Notes: <number>
To facilitate referencing and scaling, you need :
a tape measure;
a compass (to orient the model);
a caliper (to measure the thickness of the carton board or the rubber mat);
a quick reference guide to facilitate scaling;
an aplomb line;
cut-out numbers and letters (to establish the grid once the model is completed).

## Slide 16: P3DM logistics
P3DM logistics are complex because facilitators have to:
  convene 20-30 people at a time;
  accommodate and feed them for 1-2 days;
  ensure that participants represent adjacent villages to facilitate cross-verification;
  ensure that all have a role to play during the workshop.
Notes: <number>
Logistics are better addressed in Module M07, but in the case of P3DM it is better to know that …

## Slide 17: Manufacturing the Blank Model
The youth at work
Notes: <number>

## Slide 18: Tracing, cutting and pasting
Images by Giacomo Rambaldi
Notes: <number>
Split participants into three groups. Group I traces single contours from the base map on to carton board sheets. Group II cuts out the sheets. Each sheet represents a contour. Group III pastes contours on top of each other, making sure that their placement is correct.

## Slide 19: Data Input
The turn for the custodians of knowledge
Notes: <number>

## Slide 20: Orientation, here we are!
Image by Giacomo Rambaldi
Notes: <number>

## Slide 21: Transfer of spatial knowledge
Image by Giacomo Rambaldi
Notes: <number>

## Slide 22: Transfer of spatial knowledge
Image by Giacomo Rambaldi
Notes: <number>

## Slide 23: Data Extraction
Notes: <number>

## Slide 24: Data extraction
This topic is addressed in detail in M10U04
Notes: <number>

## Slide 25: Data management
Thematic maps,
GIS and database
information
Cross-checking and validating
Comparing data from different sources
Plotting thematic maps
Cartographic processing
Digitising, organising and editing data
Extracting data from
the 3D model
Various purposes
Notes: <number>