## Slide 1: Interpreting Aerial Photos and Satellite Images
By: J.Verplanke, ITC
Unit: M11U03
Notes: <number>
Study the Handout for Trainee before using this presentation.

## Slide 2: Image interpretation
How is information extracted from images?
  visual image interpretation (in this Unit)
  semi-automatic processing by computer
Notes: <number>

## Slide 3: Image interpretation
Visual interpretation is based on relating colours and patterns to real-world features.
Images can be displayed on a computer monitor or in hard copy form.
Mapping conveys the findings.
Notes: <number>

## Slide 4: Fundamentals
Analysing an image is typically done through a combination of:
  direct and “spontaneous recognition”;
  using several clues to draw conclusions through a reasoning process (i.e. “logical inference”).
Notes: <number>

## Slide 5: Fundamentals
Spontaneous recognition refers to identifying objects or features at first glance.
Notes: <number>

## Slide 6: Fundamentals
Logical inference means that the interpreter applies reasoning.
Notes: <number>

## Slide 7: Elements
Seven interpretation elements provide guidelines to recognise certain objects:
  tone/hue
  texture
  pattern
  shape
  size
  height/elevation
  location/association

## Slide 8: Elements
Tone is the relative brightness in a black-and-white image. Hue refers to the colour space.
  Tonal variations are related to the amount of light reflected (or emitted).
  Variations in hue are related to spectral characteristics.
  The human eye has a greater sensitivity for hue (10,000 colours) than for tone (200 grey levels).
Notes: <number>

## Slide 9: Elements
Texture relates to the frequency of tonal change and may be described as coarse or fine, smooth or rough, etc.
Pattern refers to spatial arrangement: concentric, radial, checkerboard, rivers with their branches, patterns related to erosion, etc.
Notes: <number>

## Slide 10: Elements
Shape or form characterises the two-dimensional projection and the height of an object.
Size can be considered in a relative or absolute sense.
Notes: <number>

## Slide 11: Elements
Height is important for distinguishing among different vegetation types, building types, etc.
Location/association refers to the situation in the terrain or in relation to its surroundings.
Notes: <number>

## Slide 12: Elements
Tone or hue can be defined for a single pixel.
Texture is defined for a group of adjacent pixels, not for a single pixel.
The other interpretation elements relate to individual objects or to a combination of objects.
Notes: <number>

## Slide 13: Mapping
The interpretation process involves delineating areas which appear similar and which are also different from other areas.
After establishing the features on the ground, “interpretation keys”’ can be constructed.
Based on these keys, an interpretation of features can be made; these are described as interpretation elements.
Notes: <number>

## Slide 14: Mapping
Notes: <number>

## Slide 15: Scale
There is a limit to what can be drawn.
In practice, polygons smaller than 5 x 5 mm should not be drawn: the "smallest allowable unit".
The scale of the image(s) thus limits the interpretation cell on the ground.
Notes: <number>

## Slide 16: Fieldwork
Maps should reflect what is actually on the ground.
Field visits observe what is there in reality.
During fieldwork, the location of boundaries is verified.
Data are gathered about features that can not be derived from remote sensing.
Notes: <number>

## Slide 17: Quality
The quality of image interpretation depends on the:
  professional experience of photo-interpreters;
  images used;
  interpretation guidelines.
These three points ensure the replicability of the work.
Notes: <number>

## Slide 18: Replicability
Replicability refers to the degree of correspondence obtained:
  by different persons for the same area; or
  by the same person for the same area at different instances.

## Slide 19: Replicability
Notes: <number>