## Slide 1: Introduction to GIS for the Purpose of Practising PGIS
Basic Functions of Geographical Information Systems
By: Jon Corbett and Kasondra White
Unit: M12U03
Notes: Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 2: Introduction
This Unit will explore:
  GIS functions;
  analytical capabilities;
  creating a map;
  querying;
  spatial analysis;
  GPS.
Notes: Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 3: Creation
Community-specific information may need to be created from scratch.
Community members may wish to apply their own naming schemes.
Community members may simply wish to edit maps that already exist.
Notes: Trainers may facilitate a discussion regarding different scenarios where communities may wish to: create maps from scratch; add to or modify existing maps; use existing maps for display purposes.
Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 4: Map scanning and digitising
The process of passing a paper map through a scanner
Map is then incorporated into a GIS and displayed/analysed
Can be scanned at high or low resolution
A preliminary step in working with GPS
Notes: Links to M12U04.
Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 5: Map scanning and digitising
May wish to convert scanned image (i.e. raster image) to a different data type (i.e. vector)
Some software packages do this automatically
Manual digitising – clicking on features on a paper map using a “puck and tablet”
Notes: Raster and vector images are explained in M12U01. This is also supplemented by Exercise No. 1 of M12U04, On-screen Digitising.
Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 6: On-screen digitising
Notes: Example of on-screen digitising over an aerial image
Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 7: Coordinate systems
Choosing a Coordinate Reference System (CRS)
Generally, the same CRS will be applied to every layer
Failure to do this will compromise the validity and analyses that can be performed
Notes: Trainers may wish to refer trainees back to the Exercise on Coordinate Reference Systems.
Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 8: Projections
Defines how 3-D information about the Earth is transferred to a 2-D surface
Necessary because spheres cannot be shown on flat surfaces without distortion
Layers displayed together must be projected in the same way
Certain analyses are only valid when certain types of projections are used
Notes: Trainers might illustrate this point in a number of ways. If they have a globe available, trainers might ask trainees to visualise the information displayed on the globe if it were to be peeled off and laid flat. How would the map have to be contorted for this to occur? Similarly, trainers might illustrate this using any round object (such as a ball) by attempting to wrap a piece of paper around it and have it lay flat. Again, have trainees observe any necessary contortions of the images.
Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 9: Georeferencing
The process of applying spatial attributes to map layers
Applies a CRS to an image
Defines relationship between objects and geographic features that are present in layers
Involves associating coordinates with features

## Slide 10: Assigning attributes
Each feature has two types of data associated with it:
  locational information (set by georeferencing)
  descriptive information (entered into Attribute Table)
Notes: Trainers may refer trainees back to Exercise on attribute data at this point if desired.
Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 11: Assigning attributes
Basic items include:
  name of feature
  area or distance of feature
  label for feature
  unique id number
Notes: Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 12: Labelling features
Label for:
  aesthetic purposes
  practical purposes
Can be turned on or off
Label properties can be edited
Notes: It may be useful to review these features on screen while speaking to trainees.
Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 13: Editing data layers
Can toggle editing on and off
Creating new points, lines and polygons
Attributing information to data points
Editing can also be turned on when working with the Attribute Table to add or manipulate data displayed in the table
Notes: Trainers may wish to complete the Exercise on Map Production at this time with trainees. Alternatively, trainers may wish to wait until the end of the presentation to complete all exercises.
Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 14: Querying
Searching for information using the Attribute Table
Find by location:
  searches according to spatial locations
Find by attribute:
  search by attributes included in the Attribute Tables
  simple and advanced searches
  multiple and comparative criteria
Notes: Trainers may wish to perform some simple searches for trainees to observe.
Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 15: Querying: find by attribute
Notes: When conducting a search by querying attributes, matches will show up as highlighted both in the Attribute Table and on the map.
Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 16: Spatial analysis
Understanding the distribution of phenomena across a geographic space
Examples include:
  relationships between smog and health
  active hunting grounds and wildlife corridors
  areas of high criminal activity
  occurrences of rare and endangered species

## Slide 17: Map overlays
Features from two input layers are overlaid
Features from each layer create new output features
Can be done in steps:
  two input layers are combined into an intermediate layer
  intermediate layer is combined with a third layer
  this continues until desired map is achieved
Notes: Trainers may demonstrate how maps can be layered by turning on and off various layers.
Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 18: Map overlays
Notes: Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 19: Spatial joins
Relating information from one layer with that contained in another
Draws all of the objects into a new layer
A new Attribute Table is created
Related to overlays

## Slide 20: Choropleth mapping
Provides a visual representation of themes or items of interest
Regions are formed based upon data associations
Criteria set by map makers
Examples include maps depicting:
  voter preference
  annual income within
  a region or country

## Slide 21: Choropleth mapping
Notes: Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 22: Buffering
Users define a zone around each point, line or polygon
Buffer forms a new polygon, which can be used in queries
A way of searching for
information according to:
  location
  proximity
Notes: Trainers may wish to do the Exercise on Spatial Analysis: Vector Data at this point.
Support the spread of “good practice” in generating, managing, analysing and communicating spatial information
<number>

## Slide 23: GPS
Uses satellites to capture points of interest
Useful for recording locations and transferring onto a map
Not always accurate
May not be able to retrieve a signal
Performance affected by weather
Lends a degree of credibility to a project

## Slide 24: Adding and analysing GPS data points
Points can be uploaded and added to maps
Points appear as a layer on their own
Map makers can attribute information to points
Map makers can perform operations based on uploaded points