## Slide 1: Documentation
Fundamentals of Audio Recording
By: Jon Corbett and Kasondra White
Unit: M14U06
Notes: <number>

## Slide 2: Introduction
Ensuring the end footage is clear and audible
Tips for making high-quality audio recordings
Recording audio in different settings
Organising and storing audio recordings
Notes: This Unit outlines some of the fundamentals of audio recording, including the steps that can be taken to ensure that the end footage is clear and audible. It will elaborate upon the process of organising and storing audio data and making use of the recordings for PGIS projects.
<number>

## Slide 3: Audio-recording tips
Cassettes used less often
Small, hand-held devices that record in a digital format are more common
Choosing a recording device – balancing cost with audio quality needs
Regardless of device, fundamentals will remain the same
Notes: Most often, audio-recording devices used in the field today record and store material in a digital format. The days of cassettes and reels have passed and have now been replaced with small hand-held devices that utilise either small internal hard drives (such as on a computer) or flash media (e.g. compact flash, secure digital). Your choice of recording device will be contingent on balancing price and audio quality needs (this Unit does not include a description of different models). This technology is changing at a blistering pace; however, the fundamentals of audio recording remain the same. This section will highlight some of these essential skills.
<number>

## Slide 4: Audio-recording tips: headphones
Allows the person who is recording to hear exactly what is being picked up
Allows for the elimination of otherwise unnoticeable sounds
Notes: Headphones (preferably the kind that cover the entire ear) allow the person recording the sound to hear exactly what the microphone is picking up (or not recording at all in some cases). This can allow for the elimination of certain sounds (e.g. someone tapping their feet) that may be unnoticeable to the naked ear, but which are being picked up on the recording.
<number>

## Slide 5: Audio-recording tips: minimise background noise
Close your eyes and listen
Soundproof studios and labs
As quiet and free of distractions as possible
Notes: In order to be fully aware of any sounds that are being picked up in the audio recording, recorders should close their eyes and listen. Ideally, sound recording should take place in soundproof studios or labs. However, these locations are rarely available, so the next best situation is to find a relatively quiet room with as little noise and distraction as possible.
<number>

## Slide 6: Audio-recording tips: manipulating the environment
Ask interviewees to turn off the TV, radio, cell phones, etc.
Background hum
Some noises cannot be removed from recordings
Notes: Interviewers should not be afraid to ask someone to turn off the TV, radio, cell phone or anything that brings unwelcome sound into the recording. Even recording in an office can be noisier than one would expect. Air conditioners, fans and computers create a constant, annoying background hum that can't be removed since it will underlie every bit of the recording.
<number>

## Slide 7: Audio-recording tips: room tone
Background noise before speaking is recorded
Also known as “ambient sound”
Record 2-3 minutes prior to the recording session
Can be used to smooth out bad edits
Notes: If a recording must take place in a noisy environment, capture two or three minutes of "room tone" at the beginning or end of any recording session. This can be done by setting the microphone up and recording while everyone present is silent. This "room tone" can be mixed into the interview later to smooth out any bad edits and make them less audible.
<number>

## Slide 8: Audio-recording tips: microphone positioning
Negative effects if too far away or too close
As close as possible, before getting so close that unwanted effects are introduced
Balance between:
  subject sound
  ambient noise
Notes: An interview can be ruined by bad microphone techniques, such as when the microphone is too close or too far away from the speaker. The further the interviewee is from the microphone, the more noise is introduced into the recording, which makes the guest sound hollow or boomy. If the microphone is too close, heavy breathing, dry mouth noises or plosives – the fancy technical word for those popping sounds people make when they say words that begin with the letter "p“ – may be audible.
The golden rule of microphone placement is to place the microphone as close as practical to the sound source without getting so close that unwanted effects are introduced. A typical hand-held microphone is usually placed at a distance of 30 cm from the speaker’s lips. Obviously, this is sometimes difficult to achieve but it is important to get as close as possible!
The aim is to achieve a good balance between the subject sound (i.e. the voice of the person talking) and the ambient noise (i.e. the other “background” noises in the room at the time). In most cases, the subject sound should be the clear focus, filled out with a moderate or low level of ambient noise. The desired balance will vary depending on the situation and the required effect. As was discussed above, recordings usually work best with few audio distractions and very low ambient noise.
<number>

## Slide 9: Audio-recording tips: holding the microphone
Hold with the fingertips.
Interviewee should not hold the microphone.
Place it 30 centimetres from the speaker’s mouth.
Omni-directional microphones work well.
Notes: When interviewing someone using a hand-held microphone, the mike should be held with the fingertips (not the whole fist), since this will reduce the handling noise and allow the interviewer to more easily tilt the microphone away to record his or her own questions. The mike can also be gently and soundlessly wiggled to nonverbally signal to the guest that they are going on too long and it's time to wrap it up. The interviewee should never hold the microphone; when this happens, the interviewer loses control of the interview and the quality of the recording.
The ideal position of the microphone depends on what type is being used, but generally the microphone should be 30 centimetres from the speaker’s mouth, at a slight angle (45 degrees) from the corner. Listen and reposition the microphone if the guest sounds off-mike or if too many plosives are audible.
There are many kinds of microphones, but generally an omni-directional microphone works well for most situations.
<number>

## Slide 10: Audio-recording tips: lavaliere microphones
Attach to subject’s clothing
Consistently pick up close-range sound
Ideal when multiple participants have their own microphones
Produce a muddier sound
Can rub against clothing
Notes: Lavaliere microphones (sometimes called lapel mikes) are usually attached to the subject's clothing using a clip. The preferred position is on or near a shirt lapel. This provides consistent pick up of close-range sounds and is ideal for interview situations in which each participant has his or her own microphone. It also means the subject doesn't have to worry about microphone technique. If there is time, the cable can be discreetly hidden in the clothing. If there is nowhere to place the microphone on the subject's chest, the collar provides an alternative.
A lavaliere microphone should be positioned so that it will not rub against your subject's clothing when he or she moves. Lapel microphones are not ideal because they produce a muddier sound, but they can be helpful for recording people who are not used to being interviewed and for whom a regular microphone may be intimidating.
<number>

## Slide 11: Audio-recording tips: listening
Sit and listen prior to recording.
Different locations may produce better results.
Close doors and windows.
Any noise should be behind the interviewer.
Notes: Before recording an interview or discussion, it is a good idea for the recorder to sit quietly in the room that will be used and simply listen to the environment. This will create an awareness of different locations in the room that may produce better results as the interviewer moves away from air vents and computers. Doors and windows should be closed, phones and computer speakers muted and cell phones turned off. If there is noise, it should be behind the interviewer so that when the microphone is pointed at the guest, it is directed away from the noise. Try not to record near windows and walls and marble floors since sound bounces off of these surfaces into the mike, creating a hollow echo.
<number>

## Slide 12: Audio-recording tips: test recordings
Record some small talk first and then review prior to the actual recording
Have guests state:
  their name
  the date
  a verbal acknowledgement of permission
Notes: It is beneficial to spend a minute recording some small talk with the subject and then listening to it before conducting the entire interview. It will be a little awkward, but if it prevents creating an unusable recording, it will be worth it. It's good to record guests saying their name, the date and a verbal acknowledgment that they are giving permission to record and edit their voice for use in a participatory mapping project. This should not be erased because it is an audio version of a release form.
<number>

## Slide 13: Audio-recording tips: keeping quiet
Be careful with encouragements such as “uh-huh” or “mmm”
Interruptions very difficult to edit out
Nodding or facial expressions a good alternative
Notes: The recorders are often asking questions and/or engaging in a conversation with the person being recorded. They need to be careful about encouraging the person being recorded by saying "uh-huh" or "mmmm" or "I see" – the things that everyone says in everyday conversation to let people know they’re listening and understanding. These interruptions will appear on the final recording and are often very difficult to edit. Instead, nodding and making facial expressions will non-verbally let the interviewee know the recorder/interviewer is engaged.
<number>

## Slide 14: Interviewing in a home
Interviews will often be conducted in the interviewee’s home.
Position devices close to interviewees.
Lift microphone off the table with a microphone stand.
Seat interviewee with back to the quietest side of the room.
Balance sound quality with comfort of interviewee.
Notes: Most often, interviews will be conducted in the interviewee’s home. The interviewee will likely have a favourite place to sit — probably in the sitting room. Any audio-recording devices that are being used should be positioned close to the interviewee. If the microphone is placed on a table, it will need to be lifted off the table using a microphone stand. If a stand is not used, there is the danger that the tabletop will reflect the sound and cause an echo or hollow effect in the final recording. Ideally, there will be a coffee table to one side of the sofa where the equipment can be positioned.
Many of these noises can be minimised by seating the interviewee with his or her back to the quietest side of the room and with the microphone positioned in front of the interviewee pointing toward the quiet area.
It is preferable that windows be closed and computer and air conditioners turned off during the interview. If possible, the ringer on the telephone should also be turned off (this includes cell phones!).
Remember that refrigerators and air conditioners turn on and off automatically and cause unnecessary noise — this is a good argument for not conducting the interview in a kitchen! Interviewers should use their best judgment as to whether or not it is advisable to stop the interview because of a loud noise, such as a passing airplane or truck. It might be more important at that moment to let the person continue talking.
The interviewer must always balance the sound quality of the interview with the general comfort and ease of the interviewee.
Too much fussing can make a person feel nervous and inhibited when it is finally time to start talking.
<number>

## Slide 15: Interviewing in a home
When deciding where an interviewee should sit, interviewers may ask:
  Is there a door that may open?
  Is there an open window?
  Is there a television or radio playing?
  Is there a refrigerator, air conditioner or computer nearby?
Notes: When considering where the interviewee should sit in a room, interviewers should pay attention to things around the room that might cause a distraction. For example interviewers may ask:
Is there a door that may open during the interview?
Is there an open window?
Is there a television or radio playing?
Are they close to a refrigerator, air conditioner or computer whose fans will impact the audio quality?
<number>

## Slide 16: Recording groups
All participants need to be clearly audible and easily identifiable.
Place recording device centrally.
Have participants introduce themselves.
Call on or thank respondents by name.
Remind participants to speak up and ensure that only one person is speaking at a time.
Notes: During participatory mapping activities, it is often necessary to record groups of people engaging in dialogue with each other and/or a recorder or facilitator. Successfully recording a group discussion requires that all participants are clearly audible and that individuals are easily identifiable. To try to achieve this, it is best to place the recording device in a central location.
If it is possible, it will be helpful to have all participants briefly introduce themselves once the group discussion has begun. This will be of assistance when trying to identify voices later on. Another tip for simplifying the identification of participants is to have the moderator call on or thank respondents by name or some other identifier.
When capturing a group discussion, the recorders will play an important role in ensuring that a high-quality audio recording is produced. They will need to remind participants to speak up if they are talking too softly and should intervene when more than one person begins to speak at a time. Furthermore, any snacks or beverages should be served during a break in the session to avoid any unnecessary noise.
<number>

## Slide 17: Storing recordings
Preserving digital information hinges on three factors:
  interoperability
  redundancy
  migration
Notes: Storing digital audio files for archival purposes – such as when recording elders’ land-related knowledge in support of participatory mapping activities – is not necessarily straightforward. The preservation of digital information hinges on three factors:
interoperability – creating digital files in standard, non-proprietary formats that can be opened on any computer using freely available software which will be supported over time;
redundancy – storing files in more than one place and creating multiple back-ups on secure media;
migration – shifting files to new media before the old media degrade and/or become obsolete and shifting files to new standard file formats before the old formats are no longer supported.
The current standard format is WAV files; it is likely that the files are already encoded (or stored) in this format.
<number>

## Slide 18: Backing up recordings
Save files on multiple external hard drives.
Create at least 2 CD or DVD discs containing audio files.
Keep materials in more than one physical location.
Check on files regularly.
When the time comes, migrate immediately.
Notes: Save audio files on multiple external hard disc drives.
Create at least two copies on CD or DVD discs that contain the audio files for each interview using two different brands of high-quality, blank media.
Keep storage materials in more than one physical location. Store CD and DVD discs in a cool, dry place away from direct sunlight.
Check files and media regularly. Transfer files to new media if any problems are suspected.
When the time comes, migrate immediately – do not delay.
Adapted from http://www.vermontfolklifecenter.org/archive/preservation-resources.shtml
<number>

## Slide 19: Using audio recordings in participatory mapping projects
Audio recordings can be:
  spliced together with photos or videos;
  used to create podcasts;
  incorporated into video documentary projects;
  used for archival purposes;
  repurposed to address different issues in the future.
Notes: Audio footage recorded during participatory mapping activities can be used for multiple purposes:
It can be spliced together with photo and video material to create digital stories.
It can be used to create podcasts for reaching a broad audience across the Internet.
It can be incorporated into video documentary products and used to support some of the advocacy elements of participatory mapping activities.
It can be used for archival purposes (and may be of great value for a community and family in later years).
It can also have unanticipated uses in the future. The material might have been recorded with a singular purpose in mind, but might be repurposed to address a different issue some time in the future.
<number>